## Slide 1: ASR4.2 handling of HW variants analysis
AUTOSAR configuration concept
  ASR.4.2 HW variants in the XML configuration structure are parameter oriented.
    In ASR 4.2 configuration type for each XML parameter/container has changed so that if focus are the parameters and not the PB containers.
    Until 4.2 the structure of the configuration XMLs was PB container oriented. Basically for each defined HW variant the user had to define one PB container with different parameters.
    HW variant-ing is now handled at parameter level allowing faster configuration of different ECU variants (i.e in Tresos is much easier to define different values for every parameter that has to be changed for one HW variant then to create a new container and add in it all the parameters even the ones that are not changed from one variant to an other)
  ASR4.2 should support variation points configuration scheme containing for each parameter:
    In order to support the current HW variant configuration scheme ASR4.2 has refined the PB configuration classes (“Loadable” and “selectable”). These attribute types are no longer used and their purpose is replaced by two boolean atribures: “Post-Build Variant Value” and “Post-Build Variant Multiplicity”.
    Either “Post-Build Variant Value” or “Post-Build Variant Multiplicity” may have the value true only if “Value Configuration Class” for that parameter contains VARIANT-POST-BUILD
    “Post-Build Variant Multiplicity” is true only if “Multiplicity Configuration Class” contains VARIANT-POST-BUILD.
    “Post-Build Variant Multiplicity” = true implies that this parameter shall have different values for each HW variant.
    “Post-Build Variant Multiplicity” = false implies that this parameter shall be common to all PB configurations (i.e. is the same for all HW variants)

## Slide 2: ASR4.2 Expected Changes
  New Tresos tool is required. Technically, the new Tresos should allow the definition of HW variants (at project level) and at module level, for each parameter that has Post-Build Variant Multiplicity = true the user should define a new value specific to that HW variant.
  The tool should parse all the parameters with Post-Build Variant Multiplicity = true and generate different configuration sets (PB structures) one for each previously defined HW variant.
  This means that the PB configuration loops are now redundant.
  XDM file changes according to the new ASR specifications.
  For each ASR parameter up to 4 new attributes were added (Post-Build Variant Value, Post-Build Variant Multiplicity , Multiplicity Configuration Class, Multiplicity ). These attributes need to be integrated in the XDM files for ASR parameters as specified by the standard.
  For NON-ASR parameters the following solution shall be used: Post-Build Variant Value = true and Post-Build Variant Multiplicity = false. This means that all NON-ASR parameters will be common to all PB Variants.
  Configuration Templates must be updated and all loops for PwmChannelConfigSet should be removed. The new configuration structure will have only one container of type PwmChannelConfigSet (multiplicity of this container is set to 1 in ASR4.2)
  At this stage PB Configuration will be (almost) identical to PC configuration, but take note that the PC configuration in reality is incorrect for AUTOSAR standard point of view. It may just be that in the future we will either change or remove altogether the [Mod]_Cfg.c files

## Slide 3: ASR4.2 Implementation suggestions 1
Open [Mod].xdm from ASR4.2 archive (see email attachment) for edit and open current [Mod].xdm (the one used for ASR4.0.3) for reading.
    Step 1. Select one by one parameters in ASR4.2 XDM file and search for them in 4.0.3 file.
    Step 2. Copy the missing attributes (i.e. “EDITABLE” or “INVALID”) from 4.0.3 to 4.2 XDM
    Step 3. Copy the “DESC” attributes from 4.0.3 to 4.2 for the “common” parameters
    Step 4. Copy the “@implements” comments for the common parameters.
    Step 5. Copy the “start of file comments ” from 4.0 to 4.2. This comments will be latter replaced by the comments used for file history.
          <!--
          * @file Pwm.xdm
          * @version 0.9.0
          *
          * @brief AUTOSAR Pwm - Tresos Studio plugin schema file
          * @details This file contains the schema configuration for and Pwm Tresos Studio plugin.
          -->
    This comments need to be copied just above line:
    <d:ctr type="AUTOSAR" factory="autosar"
    Step 6. Copy all other parameters from 4.0.3 xdm to 4.2 xdm (including comments) add the following line to the IMPLEMENTATIONCONFIGCLASS attribute:
    <icc:v class="PostBuildSelectable">VariantPostBuildSelectable</icc:v>
    This line will the used in the future development (currently all parameters will be treated as “Post Build Loadable”)
    Note: This is only valid for parameters that have also “VariatPostBuild” as value and not just “VariantPreCompile” and only for parameters in “[Mod]ChannelConfigSet” container.

## Slide 4: ASR4.2 Implementation suggestions 2
Handling [Mod]ChannelConfigSet:
  Currently this container is defined as a list of containers. However ASR 4.2 changed this (due to different handling of the HW variants and only one such container should exist.
  The 4.2 format removes the list of containers and thus the name of the container would appear just as it would be an other parameter under Tresos/General Tab.
  I would like to keep the tree-like structure that exist in xml files also in Tresos interface, so a workaround is needed.
  Add instructions for defining a list with one element around the [mod]ChannelConfigSet container definition (see example bellow)
    <v:lst name="PwmChannelConfigSet" type="MAP">
    <a:da name="MIN" value="1"/>
    <a:da name="MAX" value="1"/>
    <!-- @implements PwmChannelConfigSet_Object -->
    <v:ctr name="PwmChannelConfigSet" type="IDENTIFIABLE">
    <!-- PwmChannelConfig Set definition starts here…. All run-time config parameters are bellow -->
    </v:ctr>
    </v:lst>
Fixing xPath expresions.
  The XDM implementation for ASR4.2 changes the way some parameters are defined. For instance the [Mod] Notification parameters are now defined as a list of parameters and these changes transformed path to these parameters so the xPath expression used for validating values for these parameters will no longer work. To fix this issue it may be needed to add one “../” to the expression path.

## Slide 5: ASR4.2 Implementation suggestions 3
Handling [Mod]_Cfg.h, [Mod]_PBcfg.h and Macro files.
  The first implementation of 4.2 will support ONLY ONE HW Variant as Tresos version 17.0 only does not yet offer support for multiple HW variants. Because of this issue is may be possible that the following implementation proposal will not be valid once EB provide a tool capable of handling several variants.
  As [Mod]ChannelConfigSet was changed from a list of containers to a single container (see previous page), any LOOP instructions searching inside Config Set containers are obsolete.
  The XDM implementation for ASR4.2 changes the way some parameters are defined. For instance the [Mod] Notification parameters are now defined as a list of parameters and these changes transformed path to these parameters so the xPath expression used for validating values for these parameters will no longer work. To fix this issue it may be needed to add one “../” to the expression path.
  To get the values from the Parameters defined as “list of values” we will need to get the value of the first element in that list. (see reason above)
  So in case of Pwm, the following transformation has occurred:
  Note: In the future there will be one value for each HW variant but for now only one value will be used and/or defined.
  I would expect that there will be some Tresos provided function that will allow us to get the values of the parameters that belong to a certain HW variant.
/*ASR 4.0.3*/
#if (PWM_NOTIFICATION_SUPPORTED == STD_ON)
/** @brief Pwm notification function */
[!IF "node:exists('PwmNotification')"!]
[!IF "(PwmNotification = '') or (PwmNotification = 'NULL_PTR') or (PwmNotification = 'NULL')"!]
NULL_PTR
[!ELSE!]
/* @violates @ref Pwm_PBcfg_C_REF_5 Callback definition */
[!"PwmNotification"!],
[!ENDIF!]
[!ELSE!]
NULL_PTR,
[!ENDIF!]
#endif
/*ASR 4.2*/
#if (PWM_NOTIFICATION_SUPPORTED == STD_ON)
/** @brief Pwm notification function */
[!IF "node:exists(‘PwmNotification/*[1]')"!]
[!IF "(PwmNotification/*[1] = '') or (PwmNotification/*[1] = 'NULL_PTR') or (PwmNotification/*[1] = 'NULL')"!]
NULL_PTR
[!ELSE!]
/* @violates @ref Pwm_PBcfg_C_REF_5 Callback definition */
[!"PwmNotification/*[1]"!],
[!ENDIF!]
[!ELSE!]
NULL_PTR,
[!ENDIF!]
#endif

## Slide 6: ASR4.2 Implementation suggestions 4
Handling [Mod].mak files
Make files for all modules will require updates in order to avoid having a “doubled” configuration. Handling will be somewhat different from how the AUTOSAR version is handled in the code as the text inclusion/exclusion command (ifelse(M4_SRC_AR_RELEASE_REVISION,`ASR_REL_4_2_REV_0001',`dnl) will not work in make files. In this case standard make files conditions should be used for defining the Source files. For example for Pwm the following make file lines were used:
    ifeq ($(AR_RELEASE_REVISION),ASR_REL_4_2_REV_0001)
    SRC_FILES += $(MODULE_PATH)/specific/generate/include/Pwm_Cfg_42.h@mergefile=generate_PC/src/Pwm_Cfg.h\
    $(MODULE_PATH)/specific/generate/src/Pwm_Cfg_42.c@mergefile=generate_PC/src/Pwm_Cfg.c\
    $(MODULE_PATH)/specific/generate/src/Pwm_PBcfg_42.c@mergefile=generate_PB/src/Pwm_PBcfg.c\
    $(MODULE_PATH)/specific/generate/Pwm_NotifyCheck_Src_42.m@mergefile=generate_PC/Pwm_NotifyCheck_Src.m \
    $(MODULE_PATH)/specific/config/Pwm_42.xdm@mergefile=config/Pwm.xdm \
    $(foreach ECU_RES_SUBDERIVATIVE,$(ECU_RES_SUBDERIVATIVES), $(MODULE_PATH)/specific/config/Pwm_42.xdm@epdfile=$(ECU_EPD_FILE).epd,resfile=$(ECU_RES_FILE))
    else
    SRC_FILES += $(MODULE_PATH)/specific/generate/include/Pwm_Cfg.h@mergefile=generate_PC/src/Pwm_Cfg.h\
    $(MODULE_PATH)/specific/generate/src/Pwm_Cfg.c@mergefile=generate_PC/src/Pwm_Cfg.c\
    $(MODULE_PATH)/specific/generate/src/Pwm_PBcfg.c@mergefile=generate_PB/src/Pwm_PBcfg.c\
    $(MODULE_PATH)/specific/generate/Pwm_NotifyCheck_Src.m@mergefile=generate_PC/Pwm_NotifyCheck_Src.m \
    $(MODULE_PATH)/specific/config/Pwm.xdm \
    $(foreach ECU_RES_SUBDERIVATIVE,$(ECU_RES_SUBDERIVATIVES), $(MODULE_PATH)/specific/config/Pwm.xdm@epdfile=$(ECU_EPD_FILE).epd,resfile=$(ECU_RES_FILE))
    Endif
  Note: Same logic should apply for the definition of the signed files (SIGN_FILES)
For ASR4.2 duplicate XDM files are created and these files need to be removed:
  ifeq ($(AR_RELEASE_REVISION),ASR_REL_4_2_REV_0001)
  EXCL_FILES = $(foreach ECU_RES_SUBDERIVATIVE,$(ECU_RES_SUBDERIVATIVES), \
  $(ECU_EPD_FILE).xdm) \
  config/Pwm_42.xdm
  else
  EXCL_FILES = $(foreach ECU_RES_SUBDERIVATIVE,$(ECU_RES_SUBDERIVATIVES), \
  $(ECU_EPD_FILE).xdm)
  endif

## Slide 7: ASR4.2 Implementation suggestions 5
Final Observations:
  Some XDM parameters names may have been changed from ASR4.0 to ASR4.2:
    PwmDevErorDetect  PwmDevErrorDetect
    PwmClockRef  PwmMcuClockReferencePoint
    VSMD (Amdc) checking requires that the AUTOSAR mandatory parameters will be placed exactly in the required containers.
    In case of Pwm PwmMcuClockReferencePoint was initially placed in PwmeMios container (for ASR4.0) but this led to error A202 in VSMD check as this parameter was not placed in PwmChannel container as required by ASR4.2.
  There will be two versions of the configuration files (one for each ASR versions)
    XDM file:
      Pwm.xdm (for ASR4.0.3 the file will stay the same)
      Pwm_42.xdm (for ASR4.2 there will be an other file with the given name)
    Plugin config files
      Pwm_Cfg.x and Pwm_PBcfg.c (for ASR4.0.3 the files will stay the same)
      Pwm_Cfg_42.x and Pwm_PBcfg_42.c (for ASR4.2 there will be other files with the given name)
    Since the configuration plugin requires that files have “standard” names for that to happen the make file needs to be “updated” to change the ASR4.2 name to ASR4.0 name (i.e. Pwm_42.xdm to Pwm.xdm)

## Slide 8: ASR4.2 Implementation suggestions 6
Final Observations:
  MemMap includes changes for ASR4.2
  All files except configuration files ([Mod]_Cfg.x; [Mod]_PBcfg.c) shall have the following modification of the Memory Mapping inclusion, in order to comply with ASR4.2 standard (since only configuration files will be ASR version specific while all other filel should work on both versions)
    ifelse(M4_SRC_AR_RELEASE_REVISION,`ASR_REL_4_2_REV_0001',`dnl
    #include “[Mod]_MemMap.h"
    ‘,`dnl
    #include "MemMap.h"
    ')dnl
  Configuration files ([Mod]_Cfg.x; [Mod]_PBcfg.c) shall have the following modification of the Memory Mapping inclusion:
  #include “[Mod]_MemMap.h“
  where [Mod] = Pwm or Ocu or Icu or Gpt.